## Slide 1
Q1 | BEFORE ATTENTION
A 32-frame sample becomes B x 32 x 262 x 1024, then attention is factorized.
01 / 03
32 RGB frames
5 Hz
224 x 224
Frozen DINOv2
32 x 256 x 768
CLS + DINO regs removed
Per-frame corruption
x_t = s_t z_t + (1-s_t)e
one s_t per frame
Build frame tokens
6 prefix + 256 patches
all width 1024
Pre-attention tensor
B x 32 x 262 x 1024
8,384 tokens / sample
Per-frame token accounting
1
signal
1
action
4
registers
256
DINO patches
= 262 tokens / frame
Factorized attention reshapes
Spatial layers
(B x 32, 262, 1024)
Temporal layers
(B x 262, 32, 1024)
Noise and masks
- Gaussian latent noise; no patch masking
- causal + 24-frame temporal window
- 30% independent-frame temporal block
- action mask; padding excluded from loss
Sources: thesis Fig. 3.2; backbone.py; world_trainer.py; lerobot_dataset.py

## Slide 2
Q2 | MISSING ACTIONS
The base token separates 'action unavailable' from a valid zero control.
02 / 03
One shared action-token position; availability changes only the added projected component.
Action unavailable
token = b_action
Passive video, first frame,
independent frame, or action dropout
Action available
token = b_action + W a + c
Normalized 7D UR5 transition
from frame t-1 to frame t
Why not a sentinel?
0 is a valid / mean control
100 is out of distribution
Both depend on arbitrary scaling
What passive video teaches
It does not teach 'ignore motion'. It teaches visual dynamics conditioned on history with no observed robot command.
A zero-filled action plus an explicit availability bit would also be valid; this thesis did not ablate that alternative.
Sources: thesis Sec. 3.4 and 3.8; backbone.py action-token construction

## Slide 3
Q3 | CEM TRAJECTORY
The hook is allowed by the cost: CEM is endpoint-seeking, not path-following.
03 / 03
Implemented objective
J = terminal DINO MSE
+ 0.2 mean ||a_t||^2
Optimized
final visual state; small action magnitude
Not optimized
reference path; action differences; curvature; acceleration;
jerk; IK; joint limits; collisions; model uncertainty
Goal: 4 s later | Plan: 10 steps at 5 Hz = 2 s
Match the horizon
Use 20 actions for a 4 s reference at 5 Hz.
Add path smoothness
Intermediate cost plus delta-action, acceleration, and jerk penalties.
Enforce feasibility
Joint-space / IK planning, limits, workspace, and collision checks.
Close the loop
Receding-horizon MPC and uncertainty / OOD penalties.
Sources: thesis Fig. 4.6; planning objective; horizon and 5 Hz configuration